## Slide 1
RISC-V Microcontroller using Arrow DECA
Design of Microcontroller using RISC-V ISA on Arrow DECA Board

## Slide 2
Why use RISC-V?
1. Open-Source Nature
2. Customization and Scalability
3. Community

## Slide 3
Why?
There exists many open-source and proprietary microcontrollers using RISC-V ISA such as RocketChip, Open-V, etc
Two flaws for students
Lack of proper documentation and source code
Approachable source code for customization

## Slide 4
Aims and Objectives
1. To design a simple microcontroller using RISC-V ISA
2. Use VHDL
3. Test the system using sample programs
4. Provide Modularity
5. Provide proper documentation for the system

## Slide 5
Methodology
Two Parts
1. CPU Design
2. Peripheral Design

## Slide 6
CPU Design
RV32I ISA variant
Instruction | Description
add | reg=reg+reg
sub | reg=reg-reg
and | reg=reg&reg
or | reg=reg¦reg
addi | reg=reg+constant
andi | reg=reg&constant
ori | reg=reg¦constant
ld | reg=mem(address)
sd | mem(address)=reg
beq | Jump if reg=reg
bne | Jump if reg!=reg
Supported Instructions
Instruction Format

## Slide 7
CPU Design (Non-pipelined)
1. Clock
2. Program Counter
3. Instruction Memory
4. Control Unit
5. Register File
6. ALU
7. Data Memory
8. Immediate Generator
Detail Implementations are described in Chapter 3 of the report

## Slide 8
CPU Design (Pipeline)
Stages
1. Instruction Fetch (IF)
2. Instruction Decode (ID)
3. Execution (EX)
4. Memory (MEM)
5. Write Back (WB)

## Slide 9
CPU Design (Pipeline Hazards)
Pipeline Hazards
1. Data Hazard
2. Control Hazard
3. Structural Hazard
Mitigation
----------------> Data Forwarding
----------------> Data Forwarding
Detail Implementation can be found in Section 14 of Chapter 3 in the report

## Slide 10
Simulation Testings
Count(x1) | temp1(x2) | temp2(x3) | output(x4)
3 | 1 | 1 | 0
1 | 1 | 2 | 2
0 | 1 | 2 | 2

## Slide 11
Peripheral Designs
Microcontrollers require peripherals
Implemented Peripherals
1. UART – Universal Asynchronous Receiver Transmitter
2. SPI – Serial Parallel Interface
3. I2C – Inter-Integrated Circuit
4. I/O – Input/Output

## Slide 12
UART Design

## Slide 13
SPI Design

## Slide 14
I2C Design

## Slide 15
General I/O
General I/O wraps all other I/O related modules
1. General I/O
2. UART
3. SPI
4. I2C
All of the detail implementations and more testings have been documented in Chapter 4 of report

## Slide 16
Hardware Testings
Counting from 0 to 6 in Binary

## Slide 17
Hardware Testings
Input Testings

## Slide 18
Hardware Testings
Transmitting on UART1

## Slide 19
Thank You